## Slide 1
GridBox
Smart Infrastructure Control for £15
"What if a £15 microcontroller could replace a £162,000 industrial system?"
ARM + EEESoc | Hack-A-Bot 2026
Doyun Gu · Wooseong · Billy

## Slide 2
The Problem
30% of factory energy is wasted Motors run at full speed when partial load is enough
£180B/year lost to undetected equipment faults 4+ hours average downtime per fault
£162,000+ cost of industrial SCADA system 80% of small factories priced out
Small and medium factories can't afford Industry 4.0. They run blind — no monitoring, no fault detection, no optimisation. When equipment fails, they find out the hard way.

## Slide 3
Our Solution — GridBox
PICO A — Master Grid Controller IMU · PCA9685 · ADC Motor driver · Recycle path
nRF24L01+ Wireless 2.4GHz · 250kbps 32-byte datagrams
PICO B — Slave SCADA Station OLED · MAX7219 · nRF Wireless dashboard
Closed-Loop Control (every 10ms):
SENSE (ADC) → CALCULATE (KCL/KVL) → DECIDE (firmware) → ROUTE (GPIO) → VERIFY (ADC)
Demo: Smart Water Bottling Plant
Stage | Hardware | What Happens
Pump | DC Motor 1 | Fills bottles at PWM-controlled speed
Fill Valve | Servo 1 (PCA9685) | Opens/closes water flow
Conveyor | DC Motor 2 | Moves bottles along the line
Sort Gate | Servo 2 (PCA9685) | Directs good/reject bottles
Fault Detect | BMI160 IMU | Vibration monitoring (ISO 10816)
Energy Recycle | 2N2222 + Cap + LED | Captures and reuses wasted energy

## Slide 4
Technical Innovation
The Pico IS the Power Grid ADC pins = power sensors GPIO pins = electronic switches Firmware = brain that decides Closed loop = autonomous control
EEE Theory Applied Affinity Laws: P ∝ n³ KCL/KVL energy balance ISO 10816 vibration classification Current sensing: I = V/R
IMU Fault Detection £2 BMI160 replaces £18,000 equipment Detects: bearing wear, cavitation, jams, leaks
Energy Recycling GPIO routes excess power to storage LED proves concept: charge → glow → fade
Wireless SCADA 6-type datagram protocol 200+ packets, 0 errors Bidirectional: commands + telemetry
Key insight: 20% speed reduction = 49% power saving (Affinity Laws: P ∝ n³)

## Slide 5
What We Built
Metric | Result | Significance
Cost | £15 total BOM | 10,800x cheaper than industrial SCADA
Wireless | 200+ packets, 0 errors | 6 datagram types, bidirectional
Wiring | 77% complete (48/66 wires) | 10/13 tasks done
Firmware | 28 MicroPython modules | 16 master + 12 slave + C SDK
Tests | 35+ test scripts | Every component verified individually
Docs | 35+ documents | Full design doc, wiring tables, diagrams
Commits | 210+ commits | 3-person team, 24-hour hackathon
Hardware Verified:
nRF24L01+ wireless (both Picos) — SPI status 0x0E, channel read/write OK
Two-Pico wireless link — standalone master + USB slave, datagram protocol
MAX7219 7-segment display — all digits, brightness, flash animations
BMI160 IMU — I2C connected, chip ID verified
Motor driver — connected and wired via PCA9685 PWM
Recycle path — 2N2222 + capacitor + LED discharge indicator
£15 vs £162,000 — Same job, 10,800x cheaper

## Slide 6
GridBox
Smart Infrastructure Control for £15
Thank you — we're happy to take questions.
Doyun Gu · Wooseong · Billy | University of Manchester